## Slide 1: Problem Statement
Vehicle Cut-in Detection
To develop a sophisticated detection system capable of identifying potential vehicle collisions and issuing immediate warnings using advanced machine learning algorithms and computer vision techniques

## Slide 2: Unique Idea Brief (Solution)
This project introduces an innovative approach to vehicle cut-in detection Leveraging the YOLOv5 model, it ensures precise and efficient real-time vehicle detection. The system processes a video file input by converting it into frames. In each frame, the model calculates the distance between vehicles, detecting potential cut-ins when distances are critically close, and subsequently issues warnings as necessary. It significantly employs machine learning algorithms to fine tune the model and computer vision for detecting the vehicles.

## Slide 3: Features Offered
Lane Detection: Uses edge detection and line drawing techniques to identify lane lines on the road.
Cut-In Detection: Identifies and highlights instances where vehicles cut into lanes, generating warnings.
Vehicle Detection: Utilizes the YOLOv5 model to detect vehicles such as cars, buses, trucks, motorcycles, scooties, and bikes.
Collision Warning: Calculates the distance between vehicles and issues warnings if they are too close to each other.

## Slide 4: Features Offered
Performance Evaluation: Measures precision, recall, and F1 score for the detection algorithm using ground truth data.
Video Processing: Outputs a processed video with highlighted detections and warnings.
Distance Measurement: Measures the Euclidean distance between the centers of detected vehicles to assess proximity.
Vehicle Counting: Counts the number of vehicles detected in the video frames.
Vehicle Tracking: Tracks detected vehicles across video frames to maintain consistent identification.

## Slide 5: Process flow
1. Collecting the required dataset
Link of the dataset : https://www.kaggle.com/datasets/pkdarabi/vehicle-detection-image-dataset
2. Fine-tune the model
Re-encode Video: Ensures the input video is in a suitable format for processing.
Read Ground Truth Data: Loads ground truth vehicle locations from a CSV file for performance evaluation.

## Slide 6: Process flow
Process Video Frames: Splits the video into frames and processes each frame using the vehicle detection and tracking pipeline.
Detection and Evaluation: Detects vehicles, tracks their positions, evaluates detection performance, and calculates precision, recall, and F1 score.
Highlight and Warn: Highlights detected vehicle areas, checks for cut-in scenarios, and adds warning messages to the video.
Output Processed Video: Saves the final processed video with all detections and warnings.

## Slide 7: Architecture Diagram

## Slide 8: Technologies used
Python: For scripting and implementation.
OpenCV: For video processing and image manipulation.
YOLOv5: For vehicle detection.
MoviePy: For video handling and output.
NumPy: For numerical operations.
Pandas: For reading and handling CSV data.
PyTorch: For loading the YOLOv5 model.
Subprocess: For running FFmpeg commands.

## Slide 9: Conclusion
In conclusion, this project has developed an advanced detection system using cutting-edge machine learning and computer vision techniques. Leveraging the YOLOv5 model, it ensures precise real-time vehicle detection and identifies potential cut-in scenarios with critical proximity warnings. By integrating lane detection and vehicle classification capabilities, the system enhances safety by accurately assessing collision risks and issuing timely alerts. Through rigorous model fine-tuning, comprehensive evaluation processes, and efficient video processing, it delivers a robust solution for proactive vehicle safety management on the road.